## Slide 1
Smart Traffic Density Control System
IOT Lab Project
Sai Charan Gokha (123CS0168)
Anmol Jain (123CS0170)
Samkit Jain (123CS0171)
Group 19 :

## Slide 2
Our Goal
To design a smart system that measures real-time vehicle density in multiple lanes. This provides an accurate, live picture of the traffic load, rather than just guessing with fixed timers.
The Outcome
This live data is sent to a server via CoAP and visualized. It can then be used to dynamically adjust traffic light timings or recommend rerouting, drastically improving efficiency.
Our Solution: A Dynamic & Smart System

## Slide 3
1. Sensing
Eight ultrasonic sensors (two per lane) are used to detect vehicles entering and exiting a defined road segment.
2. Processing
An ESP32 microcontroller processes sensor data to calculate the true vehicle count (density) for each of the four lanes.
3. Reporting
The density data is sent via Wi-Fi using the lightweight CoAP protocol and visualized on a live web dashboard.
System Architecture

## Slide 4
ESP32-DevKitC v4
The "brain" of the project. Chosen for its powerful processor, built-in Wi-Fi, and ample GPIO pins to handle all 8 sensors.
HC-SR04 Ultrasonic Sensors (x8)
Used for distance measurement. They are low-cost, reliable, and provide the raw data for our density calculation.
Technology Stack: Hardware

## Slide 5
Arduino C++ (ESP32 Core)
Used to program the microcontroller, read sensor data, and perform the density-counting logic.
CoAP (coap-simple.h)
A lightweight, low-power IoT protocol (runs on UDP) perfect for sending data from constrained devices like the ESP32.
HTML, CSS, JavaScript
Built the real-time monitoring dashboard to visualize the data being sent from the ESP32.
Technology Stack: Software

## Slide 6
The "In/Out" Method
A single sensor only shows occupancy. We use two sensors per lane (Entrance and Exit) to track the actual vehicle count.
State Change Logic
Entrance Sensor (Free → Occupied): `Vehicle_Count++` Exit Sensor (Occupied → Free): `Vehicle_Count--`
Core Logic: True Density Counting

## Slide 7
CoAP stands for Constrained Application Protocol.
It is designed specifically for **IoT devices** (like our ESP32) that have limited processing power.
It runs on UDP, not TCP, making it much faster, lighter, and more efficient than HTTP for sending small, frequent data packets.
This makes it a perfect choice for an "IoT Lab" project.
»
»
»
»
Why CoAP? (IOT Lab Focus)

## Slide 8
{ "lane1_density": 2, "lane2_density": 6, "lane3_density": 1, "lane4_density": 0 }
The ESP32 formats the density counts into this simple JSON string and sends it via CoAP every second.
The Data Payload (JSON)

## Slide 9
The Live Dashboard
Real-Time Visualization

## Slide 10
Thank You
github.com/anmol0705/SmartTraffic-Density-Monitoring-System-COAP